DETAILS ABOUT THE FUNCTIONS USED IN THE CODE :

1. function [] = ForwDyn()
     USE : To calculate the forward dynamics

2. function [com_final,cm,P_final,L_final,P,L] = ForwKin(theta,T_mat,dq)
     USE : Calculate the forward kinematics of the robot

3. function [] = ForwKin_Dyn(n)
     USE : Updates the kinematics for the calculation of dynamics

4. function [T] = Hom_Trans(alp,a,d,theta)
    USE : D-H Homogeneous Tranformation Matrix

5. function [f,t,tt] = InvDyn(n)
    USE : To calculate the inverse dynamics

6. function [ ret ] = InvDyn_cal(n)
    USE : To calculate the inverse dynamics

7. function [flag,q,Dq,pos,cdl,HG] =InvKin(x,y,z,part_Id,from,adj,theta)
     USE : To calculate the inverse kinematics

8. function [flag,q,gg,pts] =
        InvKin_com(x,y,z,tg,Tr_mat,enf,from,theta,com)

    USE : To calculate the inverse kinematics on COM

9. function [flag,q,Dq,pos] = InvKin_mult(x1,y1,z1,part_Id1,x2,y2,z2,part_Id2,from,from2,adj,theta,dq)

    USE :To check and obtain the inverse kinematics solution to reach one link from some other link

10. function [flag,q] = InvKin_mult2(x,y,z,parts,from,adj)
    USE : To calculate the inverse kinematics on any link

11. function [I_s] = Is(m,c,I)
     USE : Generate spatial inertia matrix

12 . function [J] = Jacob(u,p)
    USE : Jacobian matrix generated

13. function [ J_com ] = Jacob_CoM ()
    USE : Jacobian for calculating IK of COM trajectory

14. function [x1,y1,z1] = LegTraj(l_pos,orie,sLen, sHt, sDisp, itr)
   USE : To generate the walking trajectory of the humanoid

15. function[h,AG,hG,vG] = M_mats(Tr_mat,com,dq)
    USE : AG_CMM matrix obtained

16. function [x,y,z] = Traj_1()
  USE : Trajectory generation

17. function [x,y,z] = Traj_3()
  USE : Trajectory generation

18. function [x,y,z] = Traj_4()
 USE : Trajectory generation

19. function [v,w] = calVW(pid,cid,dq,fr)
     USE : Calculate link velocity and angular velocity w.r.t global frame

20. function [flag] = collision_check()
      USE : Self collision between the parts

21. function [Idx] = find_route(part_Id,from)
      USE : Finds the route from "from"(input) to the part id

21. function [] = follow_traj(x,y,z,q,loop)
      USE : simulation function

22. function [ZMP,q] = gen_gait()
        USE : Walking gait generation

23. function[R] = gen_rand_num(arr,n)
       USE : generating a sequence of random numbers lying in the range specified by “arr “

24. function [v_hat] = hat(v)
        USE : hat operation ( sxw = hat(s)w) [hat(s) is a 3x3 matrix]

25 function ji = invsvd(j)
       USE : Calculate inverse of matrix using SVD

26. function JI = invsvd_lds(J,lamda)
       USE : Inverse of a matrix using SVD-LDS

27. function [mi] = limits_2(str)
       USE : Angle limits for each base

28. function [distance varargout] = line_to_line(p1, p2, p3, p4)
       USE : Computes the minimum distance between two line segments

29. function [x,z,x_h,z_h] = new_traj(n)
       USE : Generating leg and hip trajectories

30. function d = point_to_line(pt, v1, v2)
       USE : To calculate the perpendicular distance between the point and the line
        defined by the two vectors v1,v2

31. function[] = s_d(cm,com)
       USE : To get the stick figure

32. function [] = sample_draw(p)
      USE : generate the stick figures

33. function [v,w] = standing_vel(dq)
      USE : To calculate the velocities during standinga and walking

34. function [v,w] = walking_vel(dq)
     USE : To calculate the velocities during walking

LIST OF VARIOUS PARAMETERS USED IN THE CODE :

       1. robot.parts(n).axis_loc - denotes the axis location of robot part n

       2. robot.parts(n).joint_loc - denotes the joint location of the robot part n

        3. robot.parts(n).Z_w - denotes the rotation axis in the global frame
        n
        4. robot.parts(n).R_mat - denotes the rotation matrix of robot part n

        5. robot.parts(n).b - denotes the position of the child w.r.t
        parent in the local frame

        6. robot.parts(n).a -axis of rotation in local frame of child w.r.t
        parent

        7. robot.parts(n).ar - axis of rotation in local frame of parent w.r.t
        child

        8. robot.parts(n).br - denotes the position in the local frame of
        the child w.r.t parent frame

        9. robot.parts(n).mass - denotes the mass of the robot part n

        10. robot.parts(n).I - denotes the inertia of the robot part in the
        global frame

        11. robot.parts(n).com_g - denotes the COM of the robot part n in the
        global frame

        12. robot.parts(n).com_l - denotes the COM of the robot part n in the
        local frame

        13. robot.parts(n).v - denotes the linear velocity of the robot part n

        14. robot.parts(n).w - denotes the angular velocity of the
        robot part n

        15. robot.parts(n).P - denotes the linear momentum of the robot
        part n

        16. robot.parts(n).L - denotes the angular momentum of the robot
        part n

        17. robot.parts(n).dq - denotes the change of the angle of the robot
        link

        18. robot.parts(n).ddq -denotes the angular acceleration of the part n
        of the robot

        19. P_Id - denotes the parent Id

        20 C_Id -denotes the child Id

        21 Xs - denotes the transformation matrix for linear
        and angular momentum

        22 Is - Spatial matrix

        23 w0 - Spatial angular velocity

        24. v0 - Linear angular velocity
        25.P0 -Spatial Linear momentum
       26 L0 - Spatial angular momentum
       27. u -Joint torque
       30 Id - Part_id
       31* Xpg

       32* dw

  32* dv0

  33* sw

  34* sv

   35* dw0

   36* f1

   37 * t1

   38 * tt1

    39* f0

   40* t0

    41* tt0